## Slide 1: Lecture 3

## Slide 2: Diff b/w RAM and Registers
Registers are used to hold data immediately applicable to the operation at hand
Main Memory is used to hold data that would be needed in near future
A bus is a collection of wires. Through bus the CPU is able to extract or read data from main memory by supplying the address.
Also CPU can write data into memory by providing the address or destination of the cell

## Slide 3: Sec 2.3 Program Execution Cycle
A computer follows a program stored in Main memory by copying one instruction at a time from memory to control unit
Once in the Control Unit each instruction is decoded and obeyed
The order in which the instructions are fetched from memory correspond to the order in which they are stored in memory unless specified by JUMP

## Slide 4: Machine Cycle
Control Unit continually repeat a set of steps known as Machine Cycle that are:
Fetch
Decode
Execute

## Slide 5: What is Fetch ??
During the Fetch the Control Unit requests the Main Memory to provide it with the instruction next to be executed.
The Control Unit knows the instruction address because it is kept in the Program Counter
The Control Unit places the instruction received from memory in its Instruction Register and then increments the PC

## Slide 6: What is Decode ??
With the instruction now in the IR the control unit decodes the instruction, which involves breaking it up into Op-code and Operands.
Op-code is the number that indicates the machine instruction that needs to be executed.
Operands are those that would be manipulated by the execution of the instruction

## Slide 7
Figure 2.5 The composition of an instruction for the machine in Appendix C

## Slide 8
Figure 2.6 Decoding the instruction 35A7

## Slide 9
Figure 2.7 An encoded version of the instructions in Figure 2.2

## Slide 10: What is Execute ??
The Control Unit then executes the instruction by activating the proper circuitry to perform the requested task
Example:
If the instruction is LOAD from memory the CU causes the load to occur
When the Execute is over the Control Unit begins the cycle again

## Slide 11: What About the JUMP Instruction ??
There are two kinds of Jump Conditional and Unconditional Jumps
Conditional Jump would be executed only if certain condition is met
Example
If I have instruction B43C then B is the opcode for jump , 4 stands for Register R4 , 3C is the memory address
???????????????????????????????? 

## Slide 12
This means that the Control Unit would first compare the contents of Register 4 with Register 0 if both are equal then the Control would put the address 3C into PC.
Thus Program Execution would be altered and the instructions in between would be skipped.
However if R0 and R4 are not equal then normal execution would be continued.

## Slide 13
Figure 2.9 Decoding the instruction B258

## Slide 14: An Example of Program Execution
Suppose I have written the following High Level Language Instuction
a:= b+c
Now a, b , c are names given to some cells of memory
Suppose the address of
a is B2
b is C3
c is AA
Simplified :
Load the value stored in address C3 in some register
Load the value stored in address AA in some registers
Add both the registers and store their answer in the third register
Put Back / Store the answer in the main memory at address B2
Stop/ Halt the instruction

## Slide 15: Machine Instructions
Single High Level instructions gets translated into one or more Machine Level Instructions
Thus Machine Instructions would be:
15C3 : Load R5 with the contents of b
16AA : Load R6 with the content of c
5056 : Add R5, R6 and store their result in R0
30B2 : Store the result saved in R0 to address B2
C000: Halt

## Slide 16: An Example of Program Execution (cont….)
Address | Content
A0 | 15
A1 | C3
.A2 | 16
.A3 | AA
A4 | 50
A5 | 56
A6 | 30
A7 | B2
A8 | C0
A9 | 00
. | ?
AA | 09
Address | Content
B0 | ?
. | ?
B2 | ?
. | ?
. | ?
. | ?
. | ?
. | ?
C3 | 02
. | ?
.. | ?

## Slide 17
At first PC would be A0 IR would be empty
-------------------------------------------------------
PC : A2 IR: 15C3
Step 1: R5 would contain 2
-------------------------------------------------------
PC: A4 IR : 16AA
Step 2: R6 would contain 9
--------------------------------------------------------
PC: A6 IR: 5056
Step 3: R0 would contain B
---------------------------------------------------------
PC : A8 IR: 30B2
Step 4: Next value B would be copied to location B2
-----------------------------------------------------------------
PC: AA IR: C000
Step 5: Halt
In the end B2 i.e memory a would be containing the result