## Slide 1: Lecture # 7

## Slide 2: Topics
Storage Techniques of Bits
Mass Storage
Disk System Performance
File
Storing Fractions
Data Compression
Communication Errors

## Slide 3: Storage of Bits
Gate: A device that computes a Boolean operation
  Often implemented as (small) electronic circuits in which voltage levels indicate 0’s and 1’s
  Provide the building blocks from which computers are constructed
  VLSI (Very Large Scale Integration)

## Slide 4
Figure 1.2 A pictorial representation of AND, OR, XOR, and NOT gates as well as their input and output values

## Slide 5: Mass Storage
In computing, mass storage refers to the storage of large amounts of data in a persisting and machine-readable fashion.
Storage media for mass storage include hard disks, floppy disks, flash memory, magnetic disks, Optical Disks (CD’s, DVD’s), magnetic tape etc

## Slide 6
Mass storage includes devices with removable and non-removable media.
It does not include random access memory (RAM), which is volatile in that it loses its contents after power loss.

## Slide 7: Advantage over RAM
Less volatile
Large Storage Capacity

## Slide 8: Mass Storage
On-line versus off-line
Typically larger than main memory
Typically less volatile than main memory
Typically slower than main memory

## Slide 9: Mass Storage Systems
Magnetic Systems
  Disk
  Tape
Optical Systems
  CD
  DVD
Flash Drives

## Slide 10: Magnetic Disk
Thin disk with magnetic coating
Read/ write Heads
Head traverses circle called “Track”
Tracks divided into Sectors
Information of Tracks and Sectors setup by formatting disk

## Slide 11: Magnetic Disk
Lower Capacity Systems e.g Floppy Disk
High Capacity Systems e.g Hard Disk
Hard Disk contains 5-10 disks mounted on a spindle rigidly
To allow for Faster Speed the Head is floating above the surface
“Head Crash” due to dust particles

## Slide 12: Disk System Performance
Seek Time: Time required by the R/W head to move from one track to another
Rotational Delay / Latency Time:
Half the time required by the disk to make one complete rotation
Access Time: Seek Time + Rotational Delay
Transfer Rate: rate at which data transferred to another disk

## Slide 13: Figure 1.9 A magnetic disk storage system

## Slide 14: Figure 1.10 Magnetic tape storage

## Slide 15: Figure 1.11 CD storage

## Slide 16: Files
File: A unit of data stored in mass storage system
  Fields and keyfields
Physical record versus Logical record
Buffer: A memory area used for the temporary storage of data (usually as a step in transferring the data)

## Slide 17: Figure 1.12 Logical records versus physical records on a disk